## Slide 1
Comprehensive Analysis of Performance Data for Energized Vessel Sealing Devices Using JMP Pro 12.0
Jim Pappas, Susan Roweton, and J. Bruce Dunne
Tissue Effect Research, Surgical Innovations, Advanced Energy & Stapling, Medtronic, Boulder, Colorado
Abstract
Benefits
Analysis Methods
Burst pressure is a key performance characteristic associated with the development of safe and effective energy-based vessel sealing devices. This performance characteristic is determined by known and unknown variables and include:
Device-to-Device variability
Vessel diameter and associated tissue properties
Electrical parameters (defined by device generator algorithms )
Using JMP Pro 12.0, a comprehensive analysis approach has been developed that has enhanced the understanding of variables key to optimizing device performance.
Experimental Methods
Vessel Sealing and Data Capture
Seals created on ex vivo porcine renal arteries.
Seal Performance Dashboard
Created using JSL to facilitate quick analysis of performance data for project teams.
Syringe pump
Computer running BurstLogger software
DynoLite™ camera
Sample holding fixture
Encourages the use of ALL the data captured during a vessel sealing study.
Enables an assessment of device reliability over the full range of vessel diameters using graphical analysis combined with simulation models.
Incorporates multiple factor models to develop a more comprehensive understanding of seal performance and the associated sources of variability.
Provides for a more sensitive and accurate comparison of device efficacy between groups as compared to other, more simple methods.
Reduces samples by utilizing models to estimate burst probabilities (< 600mmHg)
Helps find and resolve potential problems early in product development.
Sealed vessels infused with saline at constant rate until seal failure occurs
Burst Testing

## Slide 2
Comprehensive Analysis of Performance Data for Energized Vessel Sealing Devices Using JMP Pro 12.0
Jim Pappas, Susan Roweton, and J. Bruce Dunne
Tissue Effect Research, Surgical Innovations, Advanced Energy & Stapling, Medtronic, Boulder, Colorado
Analysis Methods
Results
Variance Components
Ability to assess contributions of individual variables to overall variability.
Results
Model Building
Created using JSL to facilitate quick analysis of performance data for project teams.
Random Effect | Group 1 | Group 2 | LF1637 | LF1737
Device within Group (s2device ) | * | 23870 (12%) | * | *
Between Seals (s2seal event ) | 113909 (56%) | 79380 (41%) | 48823 (43%) | 105195 (70%)
Within Seals: Residual (s2residual) | 90468 (44%) | 92013 (47%) | 64307 (57%) | 46066 (30%)
Total Variability (s2total) | 204377 (100%) | 195263 (100%) | 113130 (100%) | 151260 (100%)
Yi,j,k,l,n = Burst
µ = Grand Mean
Gi = Effect of ith Group (Fixed Effect: G1, G2, G3, etc.)
Dj = Effect of jth Device within Group (Random Effect: D1, D2, D3, etc.)
Vk = Effect of kth level of Vessel Diameter Category (Fixed Effect: Small, Medium, Large, Extra Large)
(GV)i,k = Effect of Group*Vessel Diameter Category Interaction
Sl = Effect of lth Seal Event within treatment combination (Random Effect)
n = 1, 2 as there are 2 replicates per seal event (i.e., 2 sides) for bust
ε = random component for experiment / residual error
Comparison of Groups
Comparison to predicate and/or competitive devices.
Source | Degrees of Freedom | F Ratio | Prob > F
Group | 3 | 52.15 | <0.0001
Vessel Diameter Category | 3 | 11.23 | <0.0001
Group * Vessel Diameter Category | 9 | 9.69 | <0.0001

## Slide 3
Comprehensive Analysis of Performance Data for Energized Vessel Sealing Devices Using JMP Pro 12.0
Jim Pappas, Susan Roweton, and J. Bruce Dunne
Tissue Effect Research, Surgical Innovations, Advanced Energy & Stapling, Medtronic, Boulder, Colorado
Next in Line: Predictive Models
Results
Next Steps
Model Comparison
JMP Pro 12.0 allowed the comparison of various models. Prediction Profiler is a valuable tool for investigating the impact of factor settings on burst performance.
Model Exploration
Numerous approaches used with validation:
Partial Least Squares (PLS)
Neural Nets
Discriminant Analysis
Partitioning: Decision Tree, Bootstrap Forest, Boosted Tree, K Nearest Neighbors
Targeted classification models that used attribute response for burst and estimated probability Burst Pressure < 600mmHg.
Methods
Reduction of Dimensionality
Addressing multicollinearity among electrical parameters using Principal Components Analysis (PCA).
Development of a database that can easily be uploaded into JMP Pro for analysis.
Validate models with additional experimental data.
Identify additional potential factors that further improve model predictions.
JSL Scripts similar to the Seal Performance Tool that illustrate relationships between electrical parameters, tissue parameters, and, ultimately, burst pressure.