## Slide 1
IM Flash produces tens of thousands of NAND flash memory wafers per week
  Each wafer visits hundreds of processing steps
  Each process step is supported by a set of tools
  Each wafer is tested for quality and performance
Quickly sourcing yield issues to tool/step is critical to operational and business success
JMP11 introduced the Response Screening platform, for large-scale analysis. Important features include:
  Fast multi-core parallel processing
  Robust methods to help deal with messy/missing data
  False Discovery Rate adjustments for multiple testing
TreeMap (space-constrained visualization of hierarchies)
  sub-units within tools, tools within steps, steps within functional areas
Interactive dashboard features to filters and switch size/color
One-click drilldown to detailed plots
JSL scripting for automated pipeline and value-added customization
  Query test and manufacturing history data from database (1 week of simulated data is used for demonstration, 1000 lots and 1000 process steps)
  User Dialog to select inputs/options
  Response Screening results pushed to TreeMap with added local data filter and column switcher interactions
  One-click drill-down implemented through column formulas
    Selected( Row State( Row() ) )
Add-in solution automatically delivered to end-users
BigYield… an interactive yield dashboard
Landon S Jensen, Principal Engineer
IM Flash Technologies, LLC
Motivation
Method
Visualization/Interaction
Implementation
References
IM Flash - A Behind the Scenes Look: How We Make Our Product
JMP® 11 Specialized Models
JMP® 11 Scripting Guide, Second Edition

## Slide 5: Response Screening (features)

## Slide 6: JSL Details